## Slide 1: Introduction to CUDA 2 of 2
Patrick Cozzi
University of Pennsylvania
CIS 565 - Fall 2015

## Slide 2: GPU Architecture Review
GPUs are specialized for
  Compute-intensive, highly parallel computation
  Graphics!
Transistors are devoted to:
  Processing
  Not:
    Data caching
    Flow control

## Slide 3: GPU Architecture Review
Image from: http://developer.download.nvidia.com/compute/cuda/3_2_prod/toolkit/docs/CUDA_C_Programming_Guide.pdf
Transistor Usage

## Slide 4: Agenda
Built-ins and functions
Scheduling threads
Memory model
Synchronizing threads
Matrix multiply revisited

## Slide 5: Functional Declarations
 | Executed on the: | Only callable from the:
__global__ void KernelFunc() | device | host
__device__ float DeviceFunc() | device | device
__host__ float HostFunc() | host | host
See Appendix B.1 in the NVIDIA CUDA C Programming Guide for more details

## Slide 6: Functional Declarations
__global__
  Must return void
__device__
  Inlined by default
See Appendix B.1 in the NVIDIA CUDA C Programming Guide for more details

## Slide 7: Functional Declarations
What do these do?
  __device__ __host__ void func()
  __global__ __host__ void func()
Notes: Device + host = creates two functions
Global + host = not allowed.

## Slide 8: Functional Declarations
What do these do?
  __device__ __host__ void func()
  __global__ __host__ void func()
Code from http://developer.download.nvidia.com/compute/cuda/3_2_prod/toolkit/docs/CUDA_C_Programming_Guide.pdf
Notes: Use __CUDA_ARCH__ to know if code is for the host or device.

## Slide 9: Functional Declarations
Global and device functions
  No recursion (except Fermi)
  No static variables
  No malloc()
We’ll see similar constraints in GLSL
Notes: Can’t take the address of a __device__ function in host code.
Can only call __device__ functions through pointers in compute capable 2.x.

## Slide 10: Vector Types
char[1–4], uchar[1–4]
short[1–4], ushort[1–4]
int[1–4], uint[1–4]
long[1–4], ulong[1–4]
longlong[1–4], ulonglong[1–4]
float[1–4]
double1, double2

## Slide 11: Vector Types
Available in host and device code
Construct with make_<type name>
int2 i2 = make_int2(1, 2);
float4 f4 = make_float4(
1.0f, 2.0f, 3.0f, 4.0f);

## Slide 12: Vector Types
Access with .x, .y, .z, and .w
int2 i2 = make_int2(1, 2);
int x = i2.x;
int y = i2.y;
No .r, .g, .b, .a, etc. like GLSL

## Slide 13: Math Functions
double and float overloads
  No vector overloads
On the host, functions use the C runtime implementation if available
See Appendix C in the NVIDIA CUDA C Programming Guide for a complete list of math functions
Notes: On the device, SFU are likely used.

## Slide 14: Math Functions
Partial list:
  sqrt, rsqrt
  exp, log
  sin, cos, tan, sincos
  asin, acos, atan2
  trunc, ceil, floor
See Appendix C in the NVIDIA CUDA C Programming Guide for a complete list of math functions

## Slide 15: Math Functions
Intrinsic function
  Device only
  Faster, but less accurate
  Prefixed with __
  __exp, __log , __sin , __pow , …
See Appendix C in the NVIDIA CUDA C Programming Guide for a complete list of math functions

## Slide 16: Scheduling Threads
Slide from David Luebke: http://s08.idav.ucdavis.edu/luebke-nvidia-gpu-architecture.pdf
Notes: G80 – 16 SMs, each with 8 SP.

## Slide 17: Scheduling Threads

## Slide 18: Scheduling Threads
Streaming Processing (SP)

## Slide 19: Scheduling Threads
Streaming Multi-Processor (SM)

## Slide 20: Scheduling Threads
Look familiar?

## Slide 21: Scheduling Threads
Slide from David Luebke: http://s08.idav.ucdavis.edu/luebke-nvidia-gpu-architecture.pdf
G80
16 SMs
Each with 8 SPs
  128 total SPs
Each SM hosts up to 768 threads
Up to 12,288 threads in flight
Notes: 16 SMs * 768 threads = 12,288 threads in flight

## Slide 22: Scheduling Threads
Slide from David Luebke: http://s08.idav.ucdavis.edu/luebke-nvidia-gpu-architecture.pdf
GT200
30 SMs
Each with 8 SPs
  240 total SPs
Each SM hosts up to
  8 blocks, or
  1024 threads
In flight, up to
  240 blocks, or
  30,720 threads
Notes: 30 SMs * 1024 threads = 30,720 threads in flight

## Slide 23: Scheduling Threads
Warp – threads from a block
  G80 / GT200 – 32 threads
  Run on the same SM
  Unit of thread scheduling
  Consecutive threadIdx values
  An implementation detail – in theory
    warpSize

## Slide 24: Scheduling Threads
Image from: http://courses.engr.illinois.edu/ece498/al/textbook/Chapter3-CudaThreadingModel.pdf
Warps for three blocks scheduled on the same SM.
Notes: A warp from any block assigned to the SM can be selected for execution based on priority.

## Slide 25: Scheduling Threads
Image from: http://bps10.idav.ucdavis.edu/talks/03-fatahalian_gpuArchTeraflop_BPS_SIGGRAPH2010.pdf
Remember this:

## Slide 26: Scheduling Threads
Slide from: http://courses.engr.illinois.edu/ece498/al/Syllabus.html

## Slide 27: Scheduling Threads
What happens if branches in a warp diverge?

## Slide 28: Scheduling Threads
Image from: http://bps10.idav.ucdavis.edu/talks/03-fatahalian_gpuArchTeraflop_BPS_SIGGRAPH2010.pdf
Remember this:

## Slide 29: Scheduling Threads
A SM on GT200 can host up to 1024 threads, how many warps is that?
If 3 blocks are assigned to an SM and each block has 256 threads, how many warps are there?
Notes: 1024 / 32 = 32 warps
(3 * 256) / 32 = 24 warps

## Slide 30: Scheduling Threads
32 threads per warp but 8 SPs per SM. What gives?
Notes: G80
More on dispatching:
GT200: http://www.realworldtech.com/page.cfm?ArticleID=RWT090808195242&p=8
Fermi: http://www.realworldtech.com/page.cfm?ArticleID=RWT093009110932&p=5

## Slide 31: Scheduling Threads
32 threads per warp but 8 SPs per SM. What gives?
When an SM schedules a warp:
  Its instruction is ready
  8 threads enter the SPs on the 1st cycle
  8 more on the 2nd, 3rd, and 4th cycles
  Therefore, 4 cycles are required to dispatch a warp

## Slide 32: Scheduling Threads
Question
  A kernel has
    1 global memory read (200 cycles)
    4 non-dependent multiples/adds
  How many warps are required to hide the memory latency?

## Slide 33: Scheduling Threads
Solution
  Each warp has 4 multiples/adds
    16 cycles
  We need to cover 200 cycles
    200 / 16 = 12.5
    ceil(12.5) = 13
  13 warps are required
Notes: Our book says 14 in Section 6.4 (Data Prefetching) on Page 113, but I believe it is a typo.

## Slide 34: Memory Model
Image from: http://courses.engr.illinois.edu/ece498/al/textbook/Chapter2-CudaProgrammingModel.pdf

## Slide 35: Memory Model
Registers
  Per thread
  Fast, on-chip, read/write access
  Increasing the number of registers used by a kernel has what affect?
Notes: Potentially decrease the number of threads (well, blocks) available to that SM for scheduling.

## Slide 36: Memory Model
Registers - G80
  Per SM
    Up to 768 threads
    8K registers
  How many registers per thread?

## Slide 37: Memory Model
Registers - G80
  8K / 768 = 10 registers per thread
  Exceeding limit reduces threads by the block
  Example: Each thread uses 11 registers, and each block has 256 threads
    How many threads can a SM host?
    How many warps can a SM host?
    What does having less warps mean?
Notes: Host 512 threads (2 blocks instead of 3)
Host 512 / 32 = 16 warps
Instead of 768 threads and 24 warps

## Slide 38: Memory Model
Local Memory
  Stored in global memory
    Copy per thread
  Used for automatic arrays
    Unless all accessed with only constant indices

## Slide 39: Memory Model
Shared Memory
  Per block
  Fast, on-chip, read/write access
  Full speed random access

## Slide 40: Memory Model
Shared Memory – G80
  Per SM
    Up to 8 blocks
    16 KB
  How many KB per block
Notes: 2 KB per block

## Slide 41: Memory Model
Shared Memory – G80
  16 KB / 8 = 2 KB per block
  Example
    If each block uses 5 KB, how many blocks can a SM host?
Notes: 16 KB / 5 KB = 3 blocks per SM

## Slide 42: Memory Model
Global Memory
  Long latency (100s cycles)
  Off-chip, read/write access
  Random access causes performance hit
  Host can read/write
  GT200
    150 GB/s
    Up to 4 GB
  G80 – 86.4 GB/s
Notes: Kepler up to 200 GB/s

## Slide 43: Memory Model
Constant Memory
  Short latency, high bandwidth, read only access when all threads access the same location
  Stored in global memory but cached
  Host can read/write
  Up to 64 KB

## Slide 44: Memory Model
Variable Declaration | Memory | Scope | Lifetime
Automatic variables other than arrays | register | thread | kernel
Automatic array variables | local | thread | kernel
__shared__ int sharedVar; | shared | block | kernel
__device__ int globalVar; | global | grid | application
__constant__ int constantVar; | constant | grid | application
See Appendix B.2 in the NVIDIA CUDA C Programming Guide for more details

## Slide 45: Memory Model
Global and constant variables
  Host can access with
    cudaGetSymbolAddress()
    cudaGetSymbolSize()
    cudaMemcpyToSymbol()
    cudaMemcpyFromSymbol()
  Constants must be declared outside of a function body
Notes: __constant__ float constData[256];
float data[256];
cudaMemcpyToSymbol(constData, data, sizeof(data));
cudaMemcpyFromSymbol(data, constData, sizeof(data))

## Slide 46: Review: Thread Hierarchies
int threadID = blockIdx.x * blockDim.x + threadIdx.x;
float x = input[threadID];
float y = func(x);
output[threadID] = y;

## Slide 47: Review: Thread Hierarchies
int threadID = blockIdx.x * blockDim.x + threadIdx.x;
float x = input[threadID];
float y = func(x);
output[threadID] = y;
Use grid and block position to compute a thread id

## Slide 48: Review: Thread Hierarchies
int threadID = blockIdx.x * blockDim.x + threadIdx.x;
float x = input[threadID];
float y = func(x);
output[threadID] = y;
Use thread id to read from input

## Slide 49: Review: Thread Hierarchies
int threadID = blockIdx.x * blockDim.x + threadIdx.x;
float x = input[threadID];
float y = func(x);
output[threadID] = y;
Run function on input: data-parallel!

## Slide 50: Review: Thread Hierarchies
int threadID = blockIdx.x * blockDim.x + threadIdx.x;
float x = input[threadID];
float y = func(x);
output[threadID] = y;
Use thread id to output result

## Slide 51: Thread Synchronization
Threads in a block can synchronize
  call __syncthreads to create a barrier
  A thread waits at this call until all threads in the block reach it, then all threads continue
Mds[i] = Md[j];
__syncthreads();
func(Mds[i], Mds[i + 1]);

## Slide 52: Thread Synchronization
Mds[i] = Md[j];
__syncthreads();
func(Mds[i], Mds[i+1]);
Mds[i] = Md[j];
__syncthreads();
func(Mds[i], Mds[i+1]);
Mds[i] = Md[j];
__syncthreads();
func(Mds[i], Mds[i+1]);
Mds[i] = Md[j];
__syncthreads();
func(Mds[i], Mds[i+1]);
Time: 0
Thread 0
Thread 1
Thread 2
Thread 3
Notes: In this example, the warp size is 2. The block size is 4.

## Slide 53: Thread Synchronization
Mds[i] = Md[j];
__syncthreads();
func(Mds[i], Mds[i+1]);
Mds[i] = Md[j];
__syncthreads();
func(Mds[i], Mds[i+1]);
Mds[i] = Md[j];
__syncthreads();
func(Mds[i], Mds[i+1]);
Mds[i] = Md[j];
__syncthreads();
func(Mds[i], Mds[i+1]);
Time: 1
Thread 0
Thread 1
Thread 2
Thread 3

## Slide 54: Thread Synchronization
Mds[i] = Md[j];
__syncthreads();
func(Mds[i], Mds[i+1]);
Mds[i] = Md[j];
__syncthreads();
func(Mds[i], Mds[i+1]);
Mds[i] = Md[j];
__syncthreads();
func(Mds[i], Mds[i+1]);
Mds[i] = Md[j];
__syncthreads();
func(Mds[i], Mds[i+1]);
Time: 1
Thread 0
Thread 1
Thread 2
Thread 3
Threads 0 and 1 are blocked at barrier

## Slide 55: Thread Synchronization
Mds[i] = Md[j];
__syncthreads();
func(Mds[i], Mds[i+1]);
Mds[i] = Md[j];
__syncthreads();
func(Mds[i], Mds[i+1]);
Mds[i] = Md[j];
__syncthreads();
func(Mds[i], Mds[i+1]);
Mds[i] = Md[j];
__syncthreads();
func(Mds[i], Mds[i+1]);
Time: 2
Thread 0
Thread 1
Thread 2
Thread 3

## Slide 56: Thread Synchronization
Mds[i] = Md[j];
__syncthreads();
func(Mds[i], Mds[i+1]);
Mds[i] = Md[j];
__syncthreads();
func(Mds[i], Mds[i+1]);
Mds[i] = Md[j];
__syncthreads();
func(Mds[i], Mds[i+1]);
Mds[i] = Md[j];
__syncthreads();
func(Mds[i], Mds[i+1]);
Time: 3
Thread 0
Thread 1
Thread 2
Thread 3

## Slide 57: Thread Synchronization
Mds[i] = Md[j];
__syncthreads();
func(Mds[i], Mds[i+1]);
Mds[i] = Md[j];
__syncthreads();
func(Mds[i], Mds[i+1]);
Mds[i] = Md[j];
__syncthreads();
func(Mds[i], Mds[i+1]);
Mds[i] = Md[j];
__syncthreads();
func(Mds[i], Mds[i+1]);
Time: 3
Thread 0
Thread 1
Thread 2
Thread 3
All threads in block have reached barrier, any thread can continue

## Slide 58: Thread Synchronization
Mds[i] = Md[j];
__syncthreads();
func(Mds[i], Mds[i+1]);
Mds[i] = Md[j];
__syncthreads();
func(Mds[i], Mds[i+1]);
Mds[i] = Md[j];
__syncthreads();
func(Mds[i], Mds[i+1]);
Mds[i] = Md[j];
__syncthreads();
func(Mds[i], Mds[i+1]);
Time: 4
Thread 0
Thread 1
Thread 2
Thread 3

## Slide 59: Thread Synchronization
Mds[i] = Md[j];
__syncthreads();
func(Mds[i], Mds[i+1]);
Mds[i] = Md[j];
__syncthreads();
func(Mds[i], Mds[i+1]);
Mds[i] = Md[j];
__syncthreads();
func(Mds[i], Mds[i+1]);
Mds[i] = Md[j];
__syncthreads();
func(Mds[i], Mds[i+1]);
Time: 5
Thread 0
Thread 1
Thread 2
Thread 3

## Slide 60: Thread Synchronization
Why is it important that execution time be similar among threads?
Why does it only synchronize within a block?
Notes: Similar execution time – load balance
Synchronize within a block – runtime can schedule threads in any order

## Slide 61: Thread Synchronization
Image from http://courses.engr.illinois.edu/ece498/al/textbook/Chapter3-CudaThreadingModel.pdf

## Slide 62: Thread Synchronization
Can __syncthreads() cause a thread to hang?

## Slide 63: Thread Synchronization
if (someFunc())
{
__syncthreads();
}
// ...

## Slide 64: Thread Synchronization
if (someFunc())
{
__syncthreads();
}
else
{
__syncthreads();
}

## Slide 65
Let’s revisit matrix multiple

## Slide 66: Matrix Multiply: CPU Implementation
Code from: http://courses.engr.illinois.edu/ece498/al/lectures/lecture3%20cuda%20threads%20spring%202010.ppt
void MatrixMulOnHost(float* M, float* N, float* P, int width)‏
{
for (int i = 0; i < width; ++i)‏
for (int j = 0; j < width; ++j)
{
float sum = 0;
for (int k = 0; k < width; ++k)
{
float a = M[i * width + k];
float b = N[k * width + j];
sum += a * b;
}
P[i * width + j] = sum;
}
}

## Slide 67: Matrix Multiply: CUDA Kernel
Code from: http://courses.engr.illinois.edu/ece498/al/textbook/Chapter2-CudaProgrammingModel.pdf
Accessing a matrix, so using a 2D block

## Slide 68: Matrix Multiply: CUDA Kernel
Code from: http://courses.engr.illinois.edu/ece498/al/textbook/Chapter2-CudaProgrammingModel.pdf
Each kernel computes one output

## Slide 69: Matrix Multiply: CUDA Kernel
Code from: http://courses.engr.illinois.edu/ece498/al/textbook/Chapter2-CudaProgrammingModel.pdf
Where did the two outer for loops in the CPU implementation go?

## Slide 70: Matrix Multiply: CUDA Kernel
Code from: http://courses.engr.illinois.edu/ece498/al/textbook/Chapter2-CudaProgrammingModel.pdf
No locks or synchronization, why?

## Slide 71: Matrix Multiply
Problems
  Limited matrix size
    Only uses one block
    G80 and GT200 – up to 512 threads per block
  Lots of global memory access

## Slide 72: Matrix Multiply
Image from http://courses.engr.illinois.edu/ece498/al/textbook/Chapter3-CudaThreadingModel.pdf
Remove size limitation
  Break Pd matrix into tiles
  Assign each tile to a block
  Use threadIdx and blockIdx for indexing

## Slide 73: Matrix Multiply
Image from http://courses.engr.illinois.edu/ece498/al/textbook/Chapter3-CudaThreadingModel.pdf
Example
  Matrix: 4x4
  TILE_WIDTH = 2
  Block size: 2x2

## Slide 74: Matrix Multiply
Pd1,0
Md2,0
Md1,1
Md1,0
Md0,0
Md0,1
Md3,0
Md2,1
Pd0,0
Md3,1
Pd0,1
Pd2,0
Pd3,0
Nd0,3
Nd1,3
Nd1,2
Nd1,1
Nd1,0
Nd0,0
Nd0,1
Nd0,2
Pd1,1
Pd0,2
Pd2,2
Pd3,2
Pd1,2
Pd3,1
Pd2,1
Pd0,3
Pd2,3
Pd3,3
Pd1,3
Image from http://courses.engr.illinois.edu/ece498/al/Syllabus.html
Example
  Matrix: 4x4
  TILE_WIDTH = 2
  Block size: 2x2

## Slide 75: Matrix Multiply
__global__ void MatrixMulKernel(
float* Md, float* Nd, float* Pd, int Width)
{
int Row = blockIdx.y * blockDim.y + threadIdx.y;
int Col = blockIdx.x * blockDim.x + threadIdx.x;
float Pvalue = 0;
for (int k = 0; k < Width; ++k)
Pvalue += Md[Row * Width + k] * Nd[k * Width + Col];
Pd[Row * Width + Col] = Pvalue;
}
Code from http://courses.engr.illinois.edu/ece498/al/Syllabus.html

## Slide 76: Matrix Multiply
__global__ void MatrixMulKernel(
float* Md, float* Nd, float* Pd, int Width)
{
int Row = blockIdx.y * blockDim.y + threadIdx.y;
int Col = blockIdx.x * blockDim.x + threadIdx.x;
float Pvalue = 0;
for (int k = 0; k < Width; ++k)
Pvalue += Md[Row * Width + k] * Nd[k * Width + Col];
Pd[Row * Width + Col] = Pvalue;
}
Code from http://courses.engr.illinois.edu/ece498/al/Syllabus.html
Calculate the row index of the Pd element and M

## Slide 77: Matrix Multiply
__global__ void MatrixMulKernel(
float* Md, float* Nd, float* Pd, int Width)
{
int Row = blockIdx.y * blockDim.y + threadIdx.y;
int Col = blockIdx.x * blockDim.x + threadIdx.x;
float Pvalue = 0;
for (int k = 0; k < Width; ++k)
Pvalue += Md[Row * Width + k] * Nd[k * Width + Col];
Pd[Row * Width + Col] = Pvalue;
}
Code from http://courses.engr.illinois.edu/ece498/al/Syllabus.html
Calculate the column index of Pd and N

## Slide 78: Matrix Multiply
__global__ void MatrixMulKernel(
float* Md, float* Nd, float* Pd, int Width)
{
int Row = blockIdx.y * blockDim.y + threadIdx.y;
int Col = blockIdx.x * blockDim.x + threadIdx.x;
float Pvalue = 0;
for (int k = 0; k < Width; ++k)
Pvalue += Md[Row * Width + k] * Nd[k * Width + Col];
Pd[Row * Width + Col] = Pvalue;
}
Code from http://courses.engr.illinois.edu/ece498/al/Syllabus.html
Each thread computes one element of the block sub-matrix

## Slide 79: Matrix Multiply
dim3 dimGrid(Width / TILE_WIDTH, Height / TILE_WIDTH);
dim3 dimBlock(TILE_WIDTH, TILE_WIDTH);
MatrixMulKernel<<<dimGrid, dimBlock>>>(
Md, Nd, Pd, TILE_WIDTH);
Invoke kernel:

## Slide 80
What about global memory access?

## Slide 81: Matrix Multiply
Limited by global memory bandwidth
  G80 peak GFLOPS: 346.5
  Require 1386 GB/s to achieve this
  G80 memory bandwidth: 86.4 GB/s
    Limits code to 21.6 GFLOPS
    In practice, code runs at 15 GFLOPS
  Must drastically reduce global memory access

## Slide 82: Matrix Multiply
Image from http://courses.engr.illinois.edu/ece498/al/Syllabus.html
M
N
P
WIDTH
WIDTH
WIDTH
WIDTH
ty
tx
Each input element is read by Width threads
Use shared memory to reduce global memory bandwidth

## Slide 83: Matrix Multiply
Image from http://courses.engr.illinois.edu/ece498/al/Syllabus.html
Break kernel into phases
  Each phase accumlates Pd using a subset of Md and Nd
  Each phase has good data locality
Md
Nd
Pd
Pdsub
TILE_WIDTH
WIDTH
WIDTH
TILE_WIDTH
TILE_WIDTH
bx
tx
0
1
TILE_WIDTH-1
2
0
1
2
by
ty
2
1
0
TILE_WIDTH-1
2
1
0
TILE_WIDTH
TILE_WIDTH
TILE_WIDTHE
WIDTH
WIDTH

## Slide 84: Matrix Multiply
Image from http://courses.engr.illinois.edu/ece498/al/Syllabus.html
Each thread
  loads one element of Md and Nd in the tile into shared memory
Md
Nd
Pd
Pdsub
TILE_WIDTH
WIDTH
WIDTH
TILE_WIDTH
TILE_WIDTH
bx
tx
0
1
TILE_WIDTH-1
2
0
1
2
by
ty
2
1
0
TILE_WIDTH-1
2
1
0
TILE_WIDTH
TILE_WIDTH
TILE_WIDTHE
WIDTH
WIDTH
m
k
bx
by
k
m

## Slide 85
Code from http://courses.engr.illinois.edu/ece498/al/Syllabus.html
__global__ void MatrixMulKernel(
float* Md, float* Nd, float* Pd, int Width)
{
__shared__ float Mds[TILE_WIDTH][TILE_WIDTH];
__shared__ float Nds[TILE_WIDTH][TILE_WIDTH];
int bx = blockIdx.x; int by = blockIdx.y;
int tx = threadIdx.x; int ty = threadIdx.y;
int Row = by * TILE_WIDTH + ty;
int Col = bx * TILE_WIDTH + tx;
float Pvalue = 0;
for (int m = 0; m < Width/TILE_WIDTH; ++m) {
Mds[ty][tx] = Md[Row*Width + (m*TILE_WIDTH + tx)];
Nds[ty][tx] = Nd[Col + (m*TILE_WIDTH + ty)*Width];
__syncthreads();
for (int k = 0; k < TILE_WIDTH; ++k)
Pvalue += Mds[ty][k] * Nds[k][tx];
__synchthreads();
}
Pd[Row*Width+Col] = Pvalue;
}

## Slide 86
Code from http://courses.engr.illinois.edu/ece498/al/Syllabus.html
__global__ void MatrixMulKernel(
float* Md, float* Nd, float* Pd, int Width)
{
__shared__ float Mds[TILE_WIDTH][TILE_WIDTH];
__shared__ float Nds[TILE_WIDTH][TILE_WIDTH];
int bx = blockIdx.x; int by = blockIdx.y;
int tx = threadIdx.x; int ty = threadIdx.y;
int Row = by * TILE_WIDTH + ty;
int Col = bx * TILE_WIDTH + tx;
float Pvalue = 0;
for (int m = 0; m < Width/TILE_WIDTH; ++m) {
Mds[ty][tx] = Md[Row*Width + (m*TILE_WIDTH + tx)];
Nds[ty][tx] = Nd[Col + (m*TILE_WIDTH + ty)*Width];
__syncthreads();
for (int k = 0; k < TILE_WIDTH; ++k)
Pvalue += Mds[ty][k] * Nds[k][tx];
__synchthreads();
}
Pd[Row*Width+Col] = Pvalue;
}
Shared memory for a
subset of Md and Nd

## Slide 87
Code from http://courses.engr.illinois.edu/ece498/al/Syllabus.html
__global__ void MatrixMulKernel(
float* Md, float* Nd, float* Pd, int Width)
{
__shared__ float Mds[TILE_WIDTH][TILE_WIDTH];
__shared__ float Nds[TILE_WIDTH][TILE_WIDTH];
int bx = blockIdx.x; int by = blockIdx.y;
int tx = threadIdx.x; int ty = threadIdx.y;
int Row = by * TILE_WIDTH + ty;
int Col = bx * TILE_WIDTH + tx;
float Pvalue = 0;
for (int m = 0; m < Width/TILE_WIDTH; ++m) {
Mds[ty][tx] = Md[Row*Width + (m*TILE_WIDTH + tx)];
Nds[ty][tx] = Nd[Col + (m*TILE_WIDTH + ty)*Width];
__syncthreads();
for (int k = 0; k < TILE_WIDTH; ++k)
Pvalue += Mds[ty][k] * Nds[k][tx];
__synchthreads();
}
Pd[Row*Width+Col] = Pvalue;
}
Width/TILE_WIDTH
Number of phases
m
Index for current phase

## Slide 88
Code from http://courses.engr.illinois.edu/ece498/al/Syllabus.html
__global__ void MatrixMulKernel(
float* Md, float* Nd, float* Pd, int Width)
{
__shared__ float Mds[TILE_WIDTH][TILE_WIDTH];
__shared__ float Nds[TILE_WIDTH][TILE_WIDTH];
int bx = blockIdx.x; int by = blockIdx.y;
int tx = threadIdx.x; int ty = threadIdx.y;
int Row = by * TILE_WIDTH + ty;
int Col = bx * TILE_WIDTH + tx;
float Pvalue = 0;
for (int m = 0; m < Width/TILE_WIDTH; ++m) {
Mds[ty][tx] = Md[Row*Width + (m*TILE_WIDTH + tx)];
Nds[ty][tx] = Nd[Col + (m*TILE_WIDTH + ty)*Width];
__syncthreads();
for (int k = 0; k < TILE_WIDTH; ++k)
Pvalue += Mds[ty][k] * Nds[k][tx];
__synchthreads();
}
Pd[Row*Width+Col] = Pvalue;
}
Bring one element each from Md and Nd into shared memory

## Slide 89
Code from http://courses.engr.illinois.edu/ece498/al/Syllabus.html
__global__ void MatrixMulKernel(
float* Md, float* Nd, float* Pd, int Width)
{
__shared__ float Mds[TILE_WIDTH][TILE_WIDTH];
__shared__ float Nds[TILE_WIDTH][TILE_WIDTH];
int bx = blockIdx.x; int by = blockIdx.y;
int tx = threadIdx.x; int ty = threadIdx.y;
int Row = by * TILE_WIDTH + ty;
int Col = bx * TILE_WIDTH + tx;
float Pvalue = 0;
for (int m = 0; m < Width/TILE_WIDTH; ++m) {
Mds[ty][tx] = Md[Row*Width + (m*TILE_WIDTH + tx)];
Nds[ty][tx] = Nd[Col + (m*TILE_WIDTH + ty)*Width];
__syncthreads();
for (int k = 0; k < TILE_WIDTH; ++k)
Pvalue += Mds[ty][k] * Nds[k][tx];
__synchthreads();
}
Pd[Row*Width+Col] = Pvalue;
}
Wait for every thread in the block, i.e., wait for the tile to be in shared memory

## Slide 90
Code from http://courses.engr.illinois.edu/ece498/al/Syllabus.html
__global__ void MatrixMulKernel(
float* Md, float* Nd, float* Pd, int Width)
{
__shared__ float Mds[TILE_WIDTH][TILE_WIDTH];
__shared__ float Nds[TILE_WIDTH][TILE_WIDTH];
int bx = blockIdx.x; int by = blockIdx.y;
int tx = threadIdx.x; int ty = threadIdx.y;
int Row = by * TILE_WIDTH + ty;
int Col = bx * TILE_WIDTH + tx;
float Pvalue = 0;
for (int m = 0; m < Width/TILE_WIDTH; ++m) {
Mds[ty][tx] = Md[Row*Width + (m*TILE_WIDTH + tx)];
Nds[ty][tx] = Nd[Col + (m*TILE_WIDTH + ty)*Width];
__syncthreads();
for (int k = 0; k < TILE_WIDTH; ++k)
Pvalue += Mds[ty][k] * Nds[k][tx];
__synchthreads();
}
Pd[Row*Width+Col] = Pvalue;
}
Accumulate subset of dot product

## Slide 91
Code from http://courses.engr.illinois.edu/ece498/al/Syllabus.html
__global__ void MatrixMulKernel(
float* Md, float* Nd, float* Pd, int Width)
{
__shared__ float Mds[TILE_WIDTH][TILE_WIDTH];
__shared__ float Nds[TILE_WIDTH][TILE_WIDTH];
int bx = blockIdx.x; int by = blockIdx.y;
int tx = threadIdx.x; int ty = threadIdx.y;
int Row = by * TILE_WIDTH + ty;
int Col = bx * TILE_WIDTH + tx;
float Pvalue = 0;
for (int m = 0; m < Width/TILE_WIDTH; ++m) {
Mds[ty][tx] = Md[Row*Width + (m*TILE_WIDTH + tx)];
Nds[ty][tx] = Nd[Col + (m*TILE_WIDTH + ty)*Width];
__syncthreads();
for (int k = 0; k < TILE_WIDTH; ++k)
Pvalue += Mds[ty][k] * Nds[k][tx];
__synchthreads();
}
Pd[Row*Width+Col] = Pvalue;
}
Why?

## Slide 92
Code from http://courses.engr.illinois.edu/ece498/al/Syllabus.html
__global__ void MatrixMulKernel(
float* Md, float* Nd, float* Pd, int Width)
{
__shared__ float Mds[TILE_WIDTH][TILE_WIDTH];
__shared__ float Nds[TILE_WIDTH][TILE_WIDTH];
int bx = blockIdx.x; int by = blockIdx.y;
int tx = threadIdx.x; int ty = threadIdx.y;
int Row = by * TILE_WIDTH + ty;
int Col = bx * TILE_WIDTH + tx;
float Pvalue = 0;
for (int m = 0; m < Width/TILE_WIDTH; ++m) {
Mds[ty][tx] = Md[Row*Width + (m*TILE_WIDTH + tx)];
Nds[ty][tx] = Nd[Col + (m*TILE_WIDTH + ty)*Width];
__syncthreads();
for (int k = 0; k < TILE_WIDTH; ++k)
Pvalue += Mds[ty][k] * Nds[k][tx];
__synchthreads();
}
Pd[Row*Width+Col] = Pvalue;
}
Write final answer to global memory

## Slide 93: Matrix Multiply
How do you pick TILE_WIDTH?
  How can it be too large?

## Slide 94: Matrix Multiply
How do you pick TILE_WIDTH?
  How can it be too large?
    By exceeding the maximum number of threads/block
      G80 and GT200 – 512
      Fermi – 1024

## Slide 95: Matrix Multiply
How do you pick TILE_WIDTH?
  How can it be too large?
    By exceeding the maximum number of threads/block
      G80 and GT200 – 512
      Fermi – 1024
    By exceeding the shared memory limitations
      G80: 16KB per SM and up to 8 blocks per SM
        2 KB per block
        1 KB for Nds and 1 KB for Mds (16 * 16 * 4)
        TILE_WIDTH = 16
        A larger TILE_WIDTH will result in less blocks

## Slide 96: Matrix Multiply
Shared memory tiling benefits
  Reduces global memory access by a factor of TILE_WIDTH
    16x16 tiles reduces by a factor of 16
  G80
    Now global memory supports 345.6 GFLOPS
    Close to maximum of 346.5 GFLOPS

## Slide 97: First-order Size Considerations in G80
Each thread block should have many threads
  TILE_WIDTH of 16 gives 16*16 = 256 threads
There should be many thread blocks
  A 1024*1024 Pd gives 64*64 = 4K Thread Blocks
Each thread block perform 2*256 = 512 float loads from global memory for 256 * (2*16) = 8K mul/add operations.
  Memory bandwidth no longer a limiting factor
Slide from http://courses.engr.illinois.edu/ece498/al/Syllabus.html